## Slide 1: Addressing Security and Privacy Challenges in User-Device Interactions
Kassem Fawaz
University of Michigan
kassemfawaz.com

## Slide 2: LOTS of Connected Devices by 2020
Notes: http://spectrum.ieee.org/tech-talk/telecom/internet/popular-internet-of-things-forecast-of-50-billion-devices-by-2020-is-outdated

## Slide 3: User-Device Interactions

## Slide 4: Hands-Free User-Device Interactions
Direct
  User  device
  Voice-based Interaction
  30% of interactions through “conversations” with smart machines
Indirect
  User  hub  device
  Bluetooth Low Energy (BLE)
  75K unique products with BLE support
User
Hub/gateway
IoT Device
Notes: https://www.branded3.com/blog/ok-google-give-stats-voice-search/
https://www.gartner.com/doc/3021226/market-trends-voice-ui-consumer
Google I/O 2016

## Slide 5: With great power comes great responsibility
(or more security and privacy issues)

## Slide 6: Security and Privacy of User-Device Interactions
Bluetooth Low Energy
Voice interactions
Hands-free interactions
Do you share my info with third parties?

## Slide 7: BLE Security
Black Hat 2016 and DEF CON 2016
  “80 % of those BLE smart devices are vulnerable to MitM attacks.”
Reverse Engineering of BLE communications
…
Notes: https://medium.com/@urish/reverse-engineering-a-bluetooth-lightbulb-56580fcb7546#.7e1kweb0w
https://www.blackhat.com/docs/us-16/materials/us-16-Jasek-GATTacking-Bluetooth-Smart-Devices-Introducing-a-New-BLE-Proxy-Tool-wp.pdf
https://threatpost.com/bluetooth-hack-leaves-many-smart-locks-iot-devices-vulnerable/119825/
https://github.com/Jeija/bluefluff
https://github.com/michael-yuji/BLE-Hacker

## Slide 8: Voice-enabled Devices Listen to Everything

## Slide 9: How Can We Deliver Privacy Notices?
Do you share my info with third parties?

## Slide 10
This Talk:
Effectively and practically wrap an additional layer of security/privacy protection on top of user-device interactions.

## Slide 11: Research Contributions in Security & Privacy
A
B
C
D
F
E
G
I
H
Android ID
Intent IPC
Phone Number
MAC Address
Service Provider
Localization Infrastructure
RSSI
Location
Service
Location-aware apps
OS level
Android Location Services
Location Access Controls
Mobile Systems
Smartphone location privacy
  [USENIX Sec ’15a, CCS ‘14]
Indoor location privacy
  [PETS ‘16]
Mobile linkage privacy
  [USENIX Sec ‘15b]
IoT Interactions
BLE-Guardian
  [USENIX Sec ‘16]
VAuth
  [Under Review]
Pribot
  [WFPN-SOUPS ‘16, Under Review]

## Slide 12: Security and Privacy of User-Device Interactions
BLE-Guardian
Access control layer to BLE-equipped devices
VAuth
Pribot
QA interface to deliver privacy notices through a conversation
Continuous authentication interface to voice-activated devices

## Slide 13: BLE-Guardian
[USENIX Sec ’16]

## Slide 14: BLE Primer
Standby: Low Power Mode. Receiver and transmitter switched ‘off’
Advertising: Used by low power ‘IoT Device’. Only transmitter required.
Scanning: Used by ‘gateway’. Receiver listens to advertising channels.
Initiating: ‘Gateway’ sends connection request
Connection: Communication over data channels.
Scanning
Connection
Advertising
Initiating
Standby

## Slide 15: BLE Privacy & Security Effectiveness
Indirect Advertisements
  Detected 214 different unique types of devices
Address Randomization
Name | Description
ihere | key finder
DEXCOMRX | Glucose monitor
Frances’s Band ea:9d | smartband
Otbeat | heart rate monitor
JS00002074 | digital pen
Device | Days observed
One | 37
Flex | 37
Zip | 37
Forerunner 920 | 36
Basis Peak | 25
Address
00:17:E9:CB:F3:61
00:17:E9:CB:F5:01
Revealing Names
Consistent Addresses
Poor Randomization

## Slide 16: BLE Privacy & Security Effectiveness
Device Pairing
Battery level
Unique identifiers
Advertise and accept connections

## Slide 17: It All Starts with the Advertisements…
Tracking User
Profiling User
Harming User
Consistent addresses, poor randomization, unique device names and identifiers
  Health situation, user’s lifestyle, behavior, preferences, and personal interests
  Fingerprinting of and unauthorized access for sensitive systems and devices

## Slide 18
Can we effectively fend off the threats to BLE-equipped devices
  in a device-agnostic manner, and
  (2) using COTS (Commercial-Off-The-Shelf) hardware only?

## Slide 19: BLE-Guardian
Device Hiding
Access Control
Adversary
BLE-Guardian
BLE-equipped Device
Authorized client

## Slide 20: Device Hiding
Jam BLE device advertisements to hide its existence
Need to learn device advertising Interval
  Otherwise jamming will be ineffective or inefficient
Advertisement
Listen

## Slide 21: Device Hiding
Advertisement session
Estimate advertising interval:

## Slide 22: Device Hiding
Monitoring interval
Max delay

## Slide 23: Device Hiding
Monitoring interval
jamming
Detect RSSI (received signal strength indication) increase
Apply jamming

## Slide 24
At this point, the target BLE device is hidden.
  How to enable access to it?

## Slide 25: Access Control
Bluetooth classic as an OOB channel.
Connection parameters to distinguish legitimate connection request.
Connection parameters
jamming
adv
Legitimate connection
data
data
Reduced Adv.
Connection request

## Slide 26: BLE-Guardian Prototype
External hardware
  Programmable BT radio
  Open source firmware
  Rx/Tx on each BT channel
User-level app
  Control BLE-Guardian
  Update firmware seamlessly

## Slide 27: Evaluation
Cut-off distance
  Less than 1m
Impact on advertising channels
  Less than 1 unnecessary jam in 20 ms in worst-case scenario
Energy overhead
  Less than 16%
Chart: d(m)
| 0 | 0.25 | 0.5 | 0.75 | 1 | 1.25 | 1.5 | 2 | 3
clear | 0 | 0.15 | 0.2 | 0.32 | 0.35 | 0.6 | 0.7 | 0.9 | 0.9
covered | 0.1 | 0.4 | 0.6 | 0.7 | 0.7 | 0.8 | 0.9 | 0.95 | 1
Chart: # Advertisers
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Column1 | 0.033444 | 0.57971 | 1.6614 | 1.9297 | 2.0669 | 5.2841 | 5.3546 | 5.6914 | 12.92 | 15.7398

## Slide 28: Summary
BLE-equipped devices enable:
  tracking, profiling and potential physical harm
Challenge: Cannot modify BLE devices post-production
Solution: BLE-Guardian
  Privacy protection for BLE device users
  Device agnostic and relies on COTS hardware
  Low overhead on advertisement channels

## Slide 29: VAuth
[under submission]
Notes: https://robertmcgrath.wordpress.com/tag/continuous-authentication-for-voice-assistants/

## Slide 30: Voice – An Emerging Interaction
While driving, cooking, exercising …
Voice assistants and voice-activated devices

## Slide 31: Voice Is an Open Channel
with repercussions …
Mangled voice attack
[Vaidya et al. ‘15, Carlini et al. ’16]
Malicious apps issuing voice commands
[ Ben Itzhak '14]
Command injection through wireless signals
[Kasmi et al. ’15]
Notes: https://www.hackread.com/4-security-vulnerabilities-in-voice-recognition-technology/Ben-Itzhak

## Slide 32: Why Not Voice Biometrics?
Notes: http://research.baidu.com/deep-voice-production-quality-text-speech-system-constructed-entirely-deep-neural-networks/

## Slide 33: VAuth – Continuous Voice Authentication
speech
Real-time matching engine
accelerometer
Mismatch
Match

## Slide 34: VAuth Prototype
  Smaller than a coin
  Sensitive (11k Hz)
  Analog-to-digital conversion
  Secure Bluetooth transmission
(a) Wireless
(b) Eyeglasses

## Slide 35: Evaluation Results
Recruited 18 users issuing 30 commands
  Three positions: (eyeglasses, earbuds, necklace)
  Two mobility scenarios: (still and jogging)
  Five languages: (English, Korean, Arabic, Persian, Chinese)
Takeaways:
  Security: almost 0% false positive rate
  Accuracy: 97% matching rate
  Overhead: 0.35s matching delay, 1 week on 500 mAh battery
Notes: Beyond 30 cm an attacker cannot use loud voice to inject vibrations on the accelerometer.

## Slide 36: Summary
Voice is an open channel
  Unauthorized access to voice-activated devices
Challenge: Need continuous authentication mechanism for voice that does not rely on signature
Solution: VAuth
  Couple the voice channel with physical assurances from on-body vibrations
  Secure, real-time and continuous voice authentication

## Slide 37: PriBot
[WFPN-SOUPS ’16, under submission]
Do you share my info with third parties?

## Slide 38: Pribot: Privacy QA System
Do you share my info with third parties?
Do you share my info with third parties?
Pribot
Question
Answer
Information about our customers is an important part of our business, and we are not in the business of selling it to others. We share customer information only as described below and with subsidiaries Amazon.com, Inc. controls that either are subject to this Privacy Notice .

## Slide 39: Challenges
Language discrepancy between user’s question and privacy policy
Word embeddings and neural networks
Lack of privacy-related Question-Answering datasets
Repurpose existing privacy policies datasets

## Slide 40: QA Approaches
Inputs:
  Q: User Question
  S: Policy Segment
Output:
  Ranked policy segments
  User-friendly summaries
Approaches:
  Semantic Vector
  Hierarchical Classifier
Similarity
Measure
Embeddings Layer
Neural Network(s)
Q
S
q1
q2
…
a1
a2
…
Embeddings Layer
Neural Network(s)
Pribot engine
Vector
Vector

## Slide 41: Online Privacy Policies Dataset
[Wilson et al. ’16]
115 annotated policies
23K annotations
1st Party Collection
Collection Mode
Purpose
3rd Party Collection
Action
Information Type
Purpose
Choice, Control
Choice Type
Choice Scope
...
Do Not Track
Policy Change
Do Not Track Policy
Notification Type
Information Type
Audience group
Specific Audiences
Security Measure
Data Security

## Slide 42: Semantic Vector Approach
Embeddings:
  Match question-answer vocabulary
Classification Task:
Embeddings
Layer
segment
w1
w2
…
CNN
+
Max-Pooling
Dense 1
Max-
Pooling
+
ReLU
Dense 2
Softmax
class
Segment Representation
Phrase | Label
If we believe in good faith that the law requires such disclosure. | Purpose : legal-requirement
… | …

## Slide 43: Need Privacy Taxonomy
Third party collection
  “third-party application providers may automatically collect real-time geographic location information or other location-based information about you and your device . . .”
First party collection
  “we automatically collect and store certain information (. . . ) including: (. . . ) your mobile device’s geographic location (specific geographic location if you’ve enabled collection of that information…”

## Slide 44: Hierarchical Classifier
1st Party Collection
Category-level Classifier
3rd Party Collection
Info Type
Purpose
Location
Financial
Collection Mode
…
Legal
Marketing
…
On-website
From 3rd party
…
…
…
…
…
…
0.15
0.06
0.11
0.13
0.06
…
…
…
P=0.5
P=0.3

## Slide 46: Twitter Dataset
Backtrack company replies to questions
120 questions about 102 companies
Real-world testing dataset
  Real user-company interactions

## Slide 47: Relevance Evaluation
Methodology
  Between subject study
  1186 respondents on MTurk
Results
  Hierarchical: 91% relevance @3
Chart: k = # of answers returned by pribot
| 1 | 2 | 3
Retrieval | 0.52 | 0.77 | 0.87
Semantic | 0.5 | 0.75 | 0.84
Hierarchical | 0.55 | 0.77 | 0.91
Notes: Example of relevant but not accurate:
thanks. Do you pass on customer addresses to 3rd parties? Got interiors catalogue addressed to me here. How did they know
Retrieval returns the following relevant but inaccurate answer:
To supply our customers with our services we need to use information about you, and some of that may be personal or private. For example we may need to know your name and address”.
The answer, which contains multiple matching terms, describes a first-party collection practice not a third-party one.

## Slide 48: Accuracy Evaluation
Methodology
  Two independent annotators
  Consolidate the annotations
  Hierarchical:
  70% of questions had accurate answers in top 3
  Highest agreement between relevance and accuracy
Chart: k = # of answers returned by pribot
| 1 | 2 | 3
Retrieval | 0.34 | 0.45 | 0.54
Semantic | 0.34 | 0.54 | 0.67
Hierarchical | 0.34 | 0.59 | 0.69

## Slide 49: Summary
Limited-UI devices and hands-free interactions
  Traditional privacy notice delivery methods do not apply
Solution: Pribot
  Answers, automatically, user free-form question from policies
  Provides answers that have high accuracy and relevance in real-time
Deployment:
  Integrate with IoT gateways for indirect hands-free interactions
  Incorporate within voice assistants for direct hands-free interactions

## Slide 50: Conclusion
The security/privacy problems of IoT are multi-faceted
This talk addresses the interactions’ aspects:
  BLE-Guardian: BLE-equipped device
  VAuth: voice-activated devices
  Pribot: UI-limited devices
More work needed on system, users, device and policy levels

## Slide 51: Future Work
IoT Security from a Distance
A Network View to IoT Security
Usable Security & Privacy
IoT Data Privacy

## Slide 52: Thank You.
kmfawaz@umich.edu
kassemfawaz.com