## Slide 1: RT-OPEX: Flexible Scheduling for Cloud-RAN Processing
Krishna C. Garikipati, Kassem Fawaz, Kang G. Shin
University Of Michigan

## Slide 2: What is Cloud-RAN*?
fronthaulnetwork
Virtualization in Radio Access Network (RAN)
Benefits
  Lower energy consumption (compute, HVAC)
  Less site visits
  faster upgrade and replacement cycles
  Advanced signal processing
* C-RAN

## Slide 3: C-RAN in Practice

## Slide 4: Deadlines
Periodic (sub)frames every 1 ms
Hard deadline of 3ms
  Transport, decode and respond to LTE uplink frame
Requires real-time scheduling
ACK
ACK
ACK
fronthaulnetwork

## Slide 5: C-RAN Scheduling
Core network
Assign basestations to computing nodes
scheduler
Assign subframes to cores
BS 0 – subframe 0
BS 1 – subframe 0
BS 0 – subframe 1
BS 1 – subframe 1
Per-node scheduler
. . .
core 0
core 1
core 2
core N
BS 0
BS 1
BS 0
BS 1

## Slide 6: State-of-the-Art
Partitioned
CloudIQ
Global
PRAN
Parallelism
WiBench
Bigstation
Assumes fixed processing time
High runtime overhead
Scheduler-agnostic
Scheduling
Architecture

## Slide 7: Real-world Traffic
Two scheduling options:
  Design for WCET  overprovision resources
  Design for average case  deadline misses
Band 17
Band 13
Max load

## Slide 8: RT-OPEX
Offers flexible scheduling for C-RAN
Combines offline partitioned scheduling with runtime parallelism (work stealing)
Achieves resource pooling at finer time scale
Avoids over-provisioning of resources

## Slide 9
E2E model
Uplink processing
Scheduling
Leverage model for processing time
Implementation
Parallelism
Deadline misses
RT-OPEX design
Evaluation Platform
Overhead
Performance gains

## Slide 10: End to End Model

## Slide 11: Uplink Processing
Model
LTE processing in software
N = # antennas K = modulation order D = bits per carrier (load) L = decoding iterations
Dominating terms
FFT, Equalization, Turbo decoding
Error term
Platform variations (kernel tasks/interrupt handling)
Comparable to benchmark stress test
GPP () | 31.4 | 169.1 | 49.7 | 93.0 | 0.992
 | 31.4 | 169.1 | 49.7 | 93.0 | 0.992
FFT, Equalization
De-mapping, De-matching
Turbo-decoding
Error

## Slide 12: Parallelism
Decoder Block
Independent w.r.t code blocks
FFT
Independent w.r.t antenna and OFDM symbols
Notes: parallelize decoding is done over code blocks of turbo decoding
each of them are independently decodable
Processing time reduced by 310𝜇𝑠

## Slide 13: Parallelism
Task Model
Divide tasks into parallel and independent subtasks
Parallel processing
Precedence constraints

## Slide 14: End-to-End Model
Assuming Tx processing starts 1ms before deadline
RTT/2
RTT/2
RTT/2
Tx processing starts

## Slide 15: Scheduling

## Slide 16: Conventional Approaches
Static
Deterministic, offline
Offers real-time guarantees
Deadline miss:
Global
Single-queue of subframes
FIFO (or EDF) de-queuing
Non-deterministic, flexible
No real-time guarantees

## Slide 17: Scheduling Gaps
WCET design + non-optimal design  gaps in execution

## Slide 18: RT-OPEX
Exploit the gaps dynamically at runtime
core is idle
core is idle

## Slide 19: RT-OPEX Migration
Local FFT
decode
Subtasks migrated to cores with enough slack time
Local processing does not wait for migrated task
  Ensures no performance degradation
  Otherwise perform recovery
Core 0
Core 4
Core 1
Core 3
Core 2
Start migration
Local FFT

## Slide 20: Implementation
& evaluation

## Slide 21: RT-OPEX Implementation
OpenAirInterface (LTE Rel 10)
  Modularize the tasks
  Abstraction of FFT, Demod, Decode
Utilize pthread library
Migration
  Data references from shared memory
Open-source
  Enables different configurations
  https://github.com/gkchai/RT-OPEX

## Slide 22: Evaluation Platform
GPP
  32-core Intel Xeon E5, 128 GB RAM, 15 MB L3 cache
  Ubuntu 14.0.4 low latency kernel
LTE data collection
  USRP to collect load of 4 cellular towers
  30000 subframes
  Replay load from each BS trace
4 BS, 2 Antennas, 10MHz LTE FDD
1 UE per BS, 100% PRB utilization
Simulated transport delay (RTT/2)

## Slide 23: Performance Evaluation
Performance Comparison
Large gaps
Narrower gaps

## Slide 24: Migration Overhead
FFT median overhead is 26
Decoding overhead is 20
Overhead = cost of transfer OAI variables from shared memory to core
Account for overhead at migration

## Slide 25: Partitioned Scheduler
RTT/2 > 400  Budget<1.6ms  subframes with MCS > 20 miss deadlines
Partitioned scheduler cannot exploit gaps

## Slide 26: Global Scheduler
Fails to deliver performance gains
Cache thrashing causes deadline performance to saturate beyond 8 cores
At MCS 27, processing time increases with more cores

## Slide 27: Conclusion
RT-OPEX: Real-Time Opportunistic Execution
  Low overhead
    Migration on top of partitioned
  Flexible to resources
    Exploits added resources for migration
  Flexible to load
    Leverages load variations to improve deadline miss rate

## Slide 28: Thank You!
Questions?

## Slide 29: RT-OPEX Performance
Lower RTT  larger gaps
Larger RTT  narrower gaps
migrate decode tasks of high MCS  deadline miss goes to zero
migrate only FFT subtasks  deadline miss reduced

## Slide 30: Transport Latency
Latency between and Radio
Fronthaul ():
  Fixed latency (~20us/Km)
Cloud network latency ():
  Switch, Ethernet and driver delay
Latency per packet
Average 0.15ms
1Gbps Ethernet to switch
1/10 Gbps Ethernet to GPP

## Slide 31: Uplink Processing
Dynamic and depends on:
MCS selection
Number of antennas
SNR of channel
2.8x increase w.r.t MCS
0.5ms increase w.r.t L
50% increase w.r.t SNR
per antenna

## Slide 32: RT-OPEX Performance
At miss rate threshold ≤ 0.01, RT-OPEX supports 4 Mbps of extra load
RTT/2 = 500

## Slide 33: RT-OPEX
Challenges
When to migrate?
What to migrate?
How to migrate?

## Slide 34: RT-OPEX