## Slide 1: Continuous Authentication for Voice Assistants
Huan Feng1, Kassem Fawaz2, Kang G. Shin3
1 Facebook Inc.
2 University of Wisconsin
3 University of Michigan

## Slide 2: Voice – An Emerging Interaction Surface
While driving, cooking, exercising …
Voice assistants and voice-activated devices

## Slide 3: Voice-enabled Devices Listen to Everything

## Slide 4: Voice Is an Open Channel
with repercussions …
Mangled voice attack
[Vaidya et al. ‘15, Carlini et al. ’16]
Malicious apps issuing voice commands
[ Ben Itzhak '14]
Command injection from inaudible signals
[Kasmi et al. ’15, Zhang et al. ‘17]

## Slide 5: Why Not Voice Biometrics?

## Slide 6: How to solve the problem?
VAuth: Continuous Voice Authentication

## Slide 7: VAuth – Continuous Voice Authentication
speech
Real-time matching engine
accelerometer
Mismatch
Match

## Slide 8: VAuth Deployability
VAuth requires wearing a security-assisting device
  Embed VAuth in existing wearable products
(a) Earbuds
(b) Eyeglasses
(c) Necklace

## Slide 9: VAuth Prototype
  Smaller than a coin
  Sensitive (11k Hz)
  Analog-to-digital conversion
  Secure Bluetooth transmission
(a) Wireless
(b) Eyeglasses

## Slide 10: Matching Algorithm
Do the accelerometer and microphone signals match?

## Slide 11: Matching Algorithm
Segment Identification
  Detect energy bumps in accelerometer signal
Per-Segment Analysis
  Compare glottal pattern for each segment
Matching Decision
  Decide whether the two signals match

## Slide 12: Segment Identification
1. Raw signals
2. Reduce abrupt movement
4. Rise in energy levels
3. Align signals
5. Acc energy envelope
Notes: Two words, male speaker, cup, luck

## Slide 13: Per-segment Analysis
Identify glottal cycles - periodic patterns in speech
Keep matching segments
Average fundamental frequency
Average fundamental frequency ∈[80𝐻𝑧, 333𝐻𝑧]
Average relative distance
Average relative distance <25%
Maximum cross correlation
Maximum cross correlation ∈[0.25, 1]
Identify glottal cycles - periodic patterns in speech
Keep matching segments

## Slide 14: Per-segment Analysis
Non–matching segment s3
Matching segment s4

## Slide 15: Matching Decision
Input: surviving segments of acc and mic signals
SVM-based classifier trained on 44 English Phonemes of one speaker
Output: boolean decision (matching/non-matching)
Decision
execute
block
Matching
Not matching

## Slide 16: Evaluation

## Slide 17: User Study
Matching Accuracy (True Positives) & False Positives
18 users issuing 30 commands under 6 scenarios
  Three positions (eyeglasses, earbuds, necklace)
  Two mobility patterns (still and jogging)
Tested with five different languages
  English (18 users), Arabic, Korean, Persian, Chinese (1 user each)

## Slide 18: User Study
English Commands
Scenario | Movement | TP(%) – 10th percentile | FP(%) 90th percentile
Earbud | Still | 100 | 0.26
 | jogging | 91.33 | 0.33
Eyeglasses | Still | 96.66 | 0.26
 | jogging | 96.66 | 0.34
Necklace | Still | 81.66 | 0.15
 | jogging | 93.33 | 0.15
  Takeaways:
  False positive cases resulted in non-intelligible commands
  Low energy signals contributed to low TP rate in one case
  Results are consistent across the four other languages

## Slide 19: Acoustic Injection Attack
Cut-off distance beyond which acc does not pick up signals over the air
Cut-off Distance of 30 cm
Exposed Accelerometer
Covered Accelerometer
Notes:   Acoustic Injection Attack (high-power sound)

## Slide 20: Delay & Energy
Tested on real wireless prototype
Delay
  Match: 300ms – 830ms, average: 364ms
  Mismatch: 230ms – 760ms, average 319ms
  Long commands ~30 words: less than 1 second
Energy
  Idle (6mA), Active (31mA) -> most on BT transmission
  Standalone wearable (500mAh, 1 week)

## Slide 21: Conclusion
Voice is an open channel Unauthorized access to voice-activated devices
Challenge: Continuous authentication mechanism for voice that does not rely on signature
Solution: VAuth Couple the voice channel with physical assurance from on-body vibrations Average: accuracy = 97%, false positive rate = 0.1% , matching delay < 1 sec.

## Slide 22: Conclusion
Voice is an open channel
  Unauthorized access to voice-activated devices
Challenge:
  Continuous authentication mechanism for voice that does not rely on signature
Solution: VAuth
  Couple the voice channel with physical assurance from on-body vibrations
  Average accuracy = 97%, false positive rate = 0.1% , matching delay < 1 sec.
Kassem Fawaz, kfawaz@wisc.edu, kassemfawaz.com

## Slide 23: Backup slides

## Slide 24: Usability Survey
Amazon Mechanical Turk Survey
952 US respondents
Two-level Survey:
  Are voice assistants secure?
  Would you use VAuth?
    In eyeglasses?
    In necklace?
    In earbud?
    Other scenario?

## Slide 25: Phoneme-level Analysis
The basic unit of English speech
  44 phonemes (20 vowels and 24 consonants) Two speakers (one male and one female) Match each acc sample against all mic samples
Microphone | Accelerometer | True Positive (%) | False Positive (%)
consonants | consonants | 90 | 0.2
consonants | vowels | - | 1.0
vowels | consonants | - | 0.2
vowels | vowels | 100 | 1.7
all | all | 94 | 0.7
  A lower-bound of whole-command matching