## Slide 1: BLE-Guardian: Protecting the Privacy of BLE Users
Kassem Fawaz*, Kyu-Han Kim†, Kang G. Shin*
*Computer Science and Engineering, University of Michigan
†Hewlett Packard Labs

## Slide 2: What is Bluetooth Low Energy?
Attractive communication technology
  Short range
  Low energy footprint
  Supported by most hosts
Currently:
  74K unique products with BLE support
2013:
  1.2 billion BLE products shipped
2020:
  2.7 billion BLE products expected
Notes: Bluetooth.org lists 74K unique products with 4.0 support1
http://www.arubanetworks.com/assets/ds/DS_LocationServices.pdf
  (PCs, smartphones, tablets, etc.) and some APs (Aruba1)

## Slide 3: BLE Primer
Standby: Low Power Mode. Receiver and transmitter switched ‘off’
Advertising: Used by low power ‘Server’. Only transmitter required.
Scanning: Used by ‘Client’. Receiver listens to advertising channels.
Initiating: ‘Server’ sends connection request
Connection: After scanning, ‘Client’ responds to ‘Server’ advertisement
Scanning
Connection
Advertising
Initiating
Standby
Notes: Say we got the slides from Jeremey

## Slide 4: BLE Advertisements
3 dedicated advertising channels:
  2402 MHz (37), 2426 MHz (38), 2480 MHz (39)
Type | Description | Frequency
ADV_DIRECT_IND | Connect to a particular device only | 3.75 ms, but only for 1.28 seconds
ADV_IND | General presence known + connections | 20ms – 10.24s
Listen
Advertisement
Notes: They enable the whole process

## Slide 5: BLE Security and Privacy
Pairing & bonding
  Prevent unauthorized access to device or secured services
Address randomization
  Prevent user tracking
Direct Advertisements
  Prevent user tracking and profiling
Notes: They enable the whole process

## Slide 6: BLE Privacy & Security Effectiveness
Passively scan for BLE advertisements
Collect:
<Timestamp, BT Address, advertisement content, RSSI>
Site | Participants | Period
Hewlett Packard Labs | 1 | 40 days
Ann Arbor | 13 | 2 months
Phone LAB/ SUNY Buffalo | 86 | 2 months
Notes: Must fill x and y after checking the traces

## Slide 7: BLE Privacy & Security Effectiveness
Indirect Advertisements
  Detected 214 different unique types of devices
Address Randomization
Name | Description
ihere | key finder
DEXCOMRX | Glucose monitor
Frances’s Band ea:9d | smartband
Otbeat | heart rate monitor
JS00002074 | digital pen
Device | Days observed
One | 37
Flex | 37
Zip | 37
Forerunner 920 | 36
Basis Peak | 25
Address
00:17:E9:CB:F3:61
00:17:E9:CB:F5:01
Revealing Names
Consistent Addresses
Poor Randomization
Notes: Devices are verbose
This is a short list
Put a table and highlight columns with takeaways

## Slide 8: BLE Privacy & Security Effectiveness
Device Pairing
Battery level
Unique identifiers
Advertise and accept connections
Notes: Screenshots obtained from Nordic app

## Slide 9: It all starts with the advertisements…
Tracking User
Consistent addresses, poor randomization, unique device names and identifiers
Notes: “threat model” slide
  Health situation (glucose monitor), user’s lifestyle (fitness trackers), preferences (brands of devices), and personal interests (toys, cameras, Pet activity trackers, etc.)
  Fingerprinting a house physical security system or security cameras, inferring user behavior from sensory values

## Slide 10: It all starts with the advertisements…
  Health situation, user’s lifestyle, behavior, preferences, and personal interests
Tracking User
Profiling User
Notes: “threat model” slide
  Health situation (glucose monitor), user’s lifestyle (fitness trackers), preferences (brands of devices), and personal interests (toys, cameras, Pet activity trackers, etc.)
  Fingerprinting a house physical security system or security cameras, inferring user behavior from sensory values

## Slide 11: It all starts with the advertisements…
  Fingerprinting of and unauthorized access for sensitive systems and devices
Tracking User
Profiling User
Harming User
Notes: “threat model” slide
  Health situation (glucose monitor), user’s lifestyle (fitness trackers), preferences (brands of devices), and personal interests (toys, cameras, Pet activity trackers, etc.)
  Fingerprinting a house physical security system or security cameras, inferring user behavior from sensory values

## Slide 12: Research Questions
Can we effectively fend off the threats to BLE-equipped devices
  in a device-agnostic manner,
  (2) using COTS (Commercial-Off-The-Shelf) hardware only, and
  (3) with as little user intervention as possible?
Notes: Health – VP example
Focus life critical systems
Vehicle
Physical security system
Industrial systems
Spice up this slide
For example, some wearable
devices might reveal a health situation (e.g., glucose monitor).
Other devices1 might reveal information about the
user’s lifestyle (fitness trackers, treadmill), preferences
(brands of wearable devices, and personal

## Slide 13: BLE-Guardian

## Slide 14: BLE-Guardian
Ubertooth One
  Programmable BT radio
  Open source firmware
  Rx/Tx on each BT channel
User-level app
  Control BLE-Guardian
  Update firmware seamlessly
Notes: Address deployment – multiple protections

## Slide 15: High-level Description
BLE-Guardian running
Connection Enabling
Authorized client
User Alert
Attacker detected
Device Hiding Module
Owner chooses target BLE device
Client Authorization
Whitelist Client
New client
Access Control Module
Access denied
Access granted

## Slide 16: Device Hiding
Jam BLE device advertisements to hide its existence
Need to learn device advertising Sequence
  Otherwise jamming will be ineffective or inefficient
Advertisement
Listen
Notes: We need all 15 permutations

## Slide 17: Device Hiding
Monitoring interval
Advertisement session
Estimate advertising interval:
Max delay

## Slide 18: Device Hiding
Monitoring interval
jamming
Detect RSSI (received signal strength indication) increase
Apply jamming and follow advertising sequence
Notes: Now, let’s take a look at this monitoring interval

## Slide 19
At this point, the target BLE device is hidden.
  How to enable access to it?

## Slide 20: Access Control
Authorization:
Bluetooth classic as an OOB channel.
Bt_addr, UUID
Attempt connection
jamming
adv
Connection request
Client authorized by user
Send pairing request
User completes pairing

## Slide 21: Access Control
Connection Enabling:
Connection parameters to distinguish legitimate connection request.
Connection parameters
jamming
adv
Legitimate connection
data
data
adv
jamming
Reduced Adv.
Connection request

## Slide 22: Evaluation

## Slide 23: Evaluation
Cut-off Distance
Attacker
BLE device
BLE-Guardian
Cut-off distance
d

## Slide 24: Evaluation
Cut-off Distance
Chart: TI CC2540
| 0 | 0.25 | 0.5 | 0.75 | 1 | 1.25 | 1.5 | 2 | 3
clear | 0 | 0.15 | 0.2 | 0.32 | 0.35 | 0.6 | 0.7 | 0.9 | 0.9
covered | 0.1 | 0.4 | 0.6 | 0.7 | 0.7 | 0.8 | 0.9 | 0.95 | 1
Chart: Galaxy S5
| 0 | 0.25 | 0.5 | 0.75 | 1 | 1.25 | 1.5 | 2 | 3
clear | 0 | 0.05 | 0.1 | 0.3 | 0.4 | 0.45 | 0.5 | 0.7 | 0.8
covered | 0 | 0.05 | 0.18 | 0.3 | 0.5 | 0.6 | 0.7 | 0.9 | 1
Adversary has to be within 1 m of BLE device to read its advertisements

## Slide 25: Evaluation
Impact on Advertising Channels
Protect single device at advertising intervals:
  20ms, 960ms, and 10.24 sec
Two devices advertising at 20 ms
15 other devices
  With varying advertising frequencies
The number of unnecessary jamming instance is minimal
unnecessary jams

## Slide 26: Evaluation
Energy Overhead
BLE-device and authorized clients
  No overhead
Smartphone as a gateway
  Idle power: 1370mW
  Overhead: less than 16%
Chart: Galaxy S5
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Column1 | 0.033444 | 0.57971 | 1.6614 | 1.9297 | 2.0669 | 5.2841 | 5.3546 | 5.6914 | 12.92 | 15.7398
Notes: *overhead does not include powering the ubertooth radio

## Slide 27: Conclusion
BLE-Guardian
  Privacy protection for BLE device users
  Device agnostic and relies on COTS hardware
  Low overhead on advertisement channels
Future work
  Explore other M2M protocols such Zigbee
  Implement without needing external hardware (need firmware access)

## Slide 28: Thank You
kmfawaz@umich.edu
kassemfawaz.com